## Slide 1: Reducing Collision Checking for Sampling-Based Motion Planning Using Graph Neural Networks Chenning Yu, Sicun Gao
ABSTRACT
We propose new learning-based methods for reducing collision checking to accelerate motion planning by training graph neural networks (GNNs) that perform path exploration and path smoothing.
The framework consists of a path exploration component that iteratively predicts collision-free edges to prioritize their exploration, and a path smoothing component that optimizes paths obtained from the exploration stage.
The approach significantly reduces collision checking and improve overall planning efficiency in challenging high-dimensional motion planning tasks.
RESULTS
PROCEDURE
Random Geometric Graphs
A graph where the nodes that are sampled from the free space, and the edges are connected by k nearest neighbor or r-disc.
Project page available at
PRELIMINARIES
We conduct the experiments on: (i) a 2D point-robot, (ii) a 6D UR5 robot, (iii) a 7D snake robot in 2D workspace, (iv) a 7D KUKA arm, (v) an extended 13D KUKA arm, (vi) and a pair of 7DoF KUKA arms.
Our approaches significantly reduce collision checking while maintaining high success rate, low path cost, and fast overall planning. The performance scales well from low-dimensional to high-dimensional problems..
Overall Framework:
Path Exploration:
Graph Neural Networks
A neural network that aggregates information from neighbors, such as:
Collision Checking
The procedure to check whether the robot collides with the obstacles w.r.t. a node or an edge in the configuration space